Parameters	Original water		No Water	Refill water		2.1g pH up	4.65g pH up		300 uS/cm	1500uS/cm
	12/3/19 15:31:25	12/19/19 / 10:30:00	12/19/19 / 12:30:00	12/19/19 / 15:50:00	12/20/19 / 09:56:37	12/20/19 / 10:35:00	12/20/19 / 11:16:00	12/20/19 13:07:37	12/20/19 / 09:02:37	12/23/19 / 01:35:37
Barometric pressure (mb)	1008	1013	1011	1008	1011	1011	1011	1009	1007.00	1013
Nitrate (mg/L)	570.20	2591	0	2814	2952	2362	2745	3147	411.60	507
Total Dissolved Solids (mg/L)	118	115	0	99	103	109	129	150	208.00	1058
Electrical Conductivity(20) (us/cm)	167	166	0	141	145	152	181	207	287.00	1472
Dissolved Oxygen (%)	99.50	102.80	86.30	97.7	96	101	97.40	93.50	98.60	101
Electrical Conductivity(25)(us/cm)	183	181	0	155	163	172	200	228	318.00	1627
Oxidation Reduction Potential (mV)	30.80	14.40	12.90	19.10	19.70	17	17	18.3	20.30	11.80
Ammonium (mg/L)	10.84	3.78	0	5.99	5.26	6.03	5.31	5.03	3.86	1.60
Temperature (degree)	22.20	22.30	21.60	24.30	21.60	21.60	21.5	21.50	21.40	21.60
Calcium (mg/L)	77.36	201/60	306.52	209.70	125.00	116.50	118.2	120	152.10	162
pH	8.49	8.62	8.73	8.5	8.54	8.54	8.54	8.55	8.56	8.60
Dissolved Oxygen (%)(mg/L)	8.68	8.70	7.58	8.30	9.39	8.80	8.17	8.39	8.48	8.69
Depth (cm)	6	3	0	2	3.00	4	4	14	13	13
Ammonia (mg/L)	1.47	0.74	0	0.95	0.74	0.83	0.76	0.75	0.59	0.27
Electrical Conductivity (us/cm)	171	173	0	151	150.0	157	191	214	298	1522
Salinity (ppt)	0.09	0.09	0.01	0.08	0.07	0.08	0.1	0.11	0.15	0.82

------------------------------------------------------------------------------------------------------------
12/19/19 10:30 Empty the tank
------------------------------------------------------------------------------------------------------------
12/19/19 15:26 Refill the tank
------------------------------------------------------------------------------------------------------------
12/20/19 9:57 add 2.1g of pH Up
12/20/19 10:37 add 4.65g of pH Up
-------------------------------------------------------------------------------------------------------------
12/20/19 13:22 add 1g GH/KH
12/20/19 14:03 stir the water
12/20/19 14:21 add 1g GH/KH
12/20/19 14:31 add 1g GH/KH
12/20/19 14:39 add 1g GH/KH
12/20/19 14:53 add 1g GH/KH
12/20/19 15:06 add 1g GH/KH
12/20/19 15:15 add 5g GH/KH
12/20/19 15:26 add 1g GH/KH
12/20/19 15:55 add 5g GH/KH (max reading:322)
12/20/19 16:39 add 1g GH/KH
------------------------------------------------------------------------------------
12/23/19 9:23 add 50g GH/KH
12/23/19 9:28 add 20g GH/KH (max reading: 1732)

12/26/19 10:33 add 2g pH down

1. 12/27/19 11am empty tank
12/27/19 12:32pm add 54x2L =108L water into main-tank (reach water level line001)
12/27/19 12:35pm add 2x2L = 4L water into sub-tank001
12/27/19 12:43pm add 15x2L = 30L water into sub-tank003 (biggest)
12/27/19 12:45pm add 2x2L = 4L water into sub-tank002
12/27/19 12:50pm turn on chiller and pump
       (main-tank reaches water level line002; sub-tank003 empty, water into main tank)
       main tank: 123L
12/27/19 12:55pm add 10x2L = 20L water into sub-tank003 (biggest)
Note: Main-tank:123L , sub-tank001: 4L , sub-tank002: 4L, sub-tank003: 20L
12/27/19 13:43 add 300ml RapidCal liquid (pH 7)
12/27/19 14:25 add 300ml RapidCal Liquid (pH10)
12/27/19 14:30 complete pH calibration
12/27/19 14:36 put probes back into tank
-----------------------------------------------------------------------------------------------------------------
2. 12/30/19 10:28 Replace water in tank
Note: Main-tank:123L , sub-tank001: 4L , sub-tank002: 4L, sub-tank003: 20L
12/30/19 11:03 Add 10L water into sub-tank003 (biggest)
------------------------------------------------------------------------------------------------------------------
3. 01/02/2020 8:54am put probs into pH7.0 calibration liquid
        01/02/2020 9:15am clean the probs with de-ionized water and put them into de-ionized water
      01/02/2020 9:19am put probes back into tank

01/02/2020 10:20am put probes into de-ionized water
01/02/2020 10:30am empty the tank
01/02/2020 10:40am add main-tank to water level line001
01/02/2020 10:42am put probes back into tank

01/02/2020 13:47 add
add 30x2L = 60L water into sub-tank003 (biggest)
add 2x2L = 4L water into sub-tank002
add 2x2L = 4L water into sub-tank001

        (7.73)
01/03/2020 10:01 add 1g pH Down (7.58)
01/03/2020 11:07 add 4.5g pH Down (7.15)
01/03/2020 13:28 add 4.5g pH Down (6.94)
01/03/2020 14:32 add 1.5g pH Down (6.86)
01/03/2020 15:04 add 0.94g pH Down (6.86)
01/03/2020 15:41 add 1.11g pH Down (6.81)
01/03/2020 16:19 add 1.5g pH Down

01/07/2020 10:54am add 10g pH Up
01/07/2020 15:25am add 10g pH Up
01/07/2020 17:16am add 10g pH Up

main-tank: 123L ; sub-tanks: 28L - 50L
Parameters	Before Replacement of water	After first Replacement of water	After second Replacement of water	After third / Replacement of water	After adding 12g pH down
	2019-12-24 / 17:00:00	2019-12-27 17:01:00	2019-12-30 / 12:01:26	2020-01-03 09:07:26
Barometric pressure (mb)	1008	1007	1013	1014
Nitrate (mg/L)	39.50	856.90	560	305
Total Dissolved Solids (mg/L)	1125	272	262	204
Electrical Conductivity(20) (us/cm)	1562	372	365	280
Dissolved Oxygen (%)	93.990	93.40	87.50	92.70
Electrical Conductivity(25)(us/cm)	1727	416	403	312
Oxidation Reduction Potential (mV)	9	119.10	94.90	68.9
Ammonium (mg/L)	0.33	0.94	0.68	0.41
Temperature (degree)	21.40	21.40	21.40	21.40
Calcium (mg/L)	199.38	70.45	74.05	93.76
pH	8.63	8.34	7.81	7.74
Dissolved Oxygen (%)(mg/L)	8.37	8.49	7.59	8.24
Depth (cm)	1	16.00	15.00	6
Ammonia (mg/L)	0.06	0.08	0.02	0.01
Electrical Conductivity (us/cm)	1614	381	379.00	291
Salinity (ppt)	0.87	0.20	0.19	0.15

------------------------------------------------------------------------------------------------------------
Please perform the following activities and report back on the Aquaread measurements:

Change to new fresh tap water to same water volume as 143 L and obtain new Aquameter readings: Record initial water parameters.

1.            Record new Aquameter readings after change of water (143L as per our SIT tank volume).

2.            pH adjustment
               (a)          Add 2.1 g of pH Up chemical and dissolve completely in tank,  and record Aquameter pH value after 30 minutes. pH value ___
               (b)          Add another 4.65 g of pH UP chemical and dissolve completely in tank, and record Aquameter pH value after 30 minutes. pH ____

3.            Electrical Conductivity (143L as per our SIT tank volume)
              (a)          Add GH/KH chemicals until the Conductivity reading shows 300 uS/cm. Record weight of chemical added:  _18__ g
               (b)          Continue adding GH/KH chemical until conductivity reading shows 1500 uS/cm. Record total weight of chemical added: __70__ g